## Slide 1
2019 European Seminar – Amsterdam, Netherlands

## Slide 2
Access Control

## Slide 4: O3 ACCESS
O3-DIN access control module
Complete Access Control System solution includes:
  O3-DIN-CPU firmware
  enteliWEB
  eSYNC
  Access specific dashboards

## Slide 5: O3-DIN-ACCESS
Provides the IO for access control for a typical single door / credential reader
IO specific to access control application
  wiegand input
  supervised circuits
  door lock outputs
No processing in the module, O3-DIN-CPU does control
IO focused firmware with higher reliability, allows O3-DIN-CPU to add on formats & functionality

## Slide 6: O3-DIN-ACCESS Module
IO interface for a typical single door / credential reader
IO specific to access control application
  Wiegand input with LED output
    26 bit
    37 bit
    37 bit facility
    Simple 32
    Custom (V4.9 firmware)
  Supervised input circuits - Door Contact and RTE
  Door lock outputs
  12V/24V power output
  Additional Universal IO - Software configurable
Supports multi-format reader from one input interface
Card reader
REX
Power in
Door
lock
Door
contact
Universal
point

## Slide 7: Architecture

## Slide 8
Typical module 15W
~75W Total

## Slide 9: Application
Typical Single Direction Door
  1 - O3-DIN-ACCESS with 12/24 electric strike, card reader, door contact, and 12/24 request to exit device
Single Direction Door with holder
  1 - O3-DIN-ACCESS with 12/24 electric strike, card reader, door contact, and 12/24 request to exit device, and 12/24VDC door holder

## Slide 10: Reader Types
Support multi format upto 200 bits on wiegand port i.e. 26 and 37 bit
Formats are in O3-DIN-CPU not the module so easy to add to formats as we go
Door lock response <250ms meeting Doherty Threshold of response (ADM was upto ~800ms)
Compact takes less space and space costs
Energy management enabled, power monitored and power supplies controlled to shed energy

## Slide 11: Where are we going?
PoE 2 Door Module Access
  CPU and 2 door IO built in
  Power all from PoE
Integrated single room controller / 4 door access controller
  O3-DIN single room CPU
  4 Module support for integration or 4 access controlled doors

## Slide 12
O3-DIN-CPU or O3-DIN-SRC?
O3-DIN-SRC
  Centralized Layout up to 4 doors
O3-DIN-CPU
  Centralized Layout up to 24 single direction doors and 5 power injectors
  Distributed Layout up to 24 single direction doors and 8 power injectors

## Slide 13: Software

## Slide 14
O3 Access System
Software
enteliSYNC
enteliWEB Access Dashboards

## Slide 15: enteliWEB Access Dashboards
Single-seat management software
Intuitive dashboards for user enrollment
Role based permissions for different users
Customizable extended access user information
GDPR compliant
Visualizations via widgets reporting live data
Customizable access activity report
Virtual Enrollment Reader

## Slide 16
enteliSYNC
Central Database – Synchronization engine,
Multi-Site functionality
Triggered by access dashboard
Virtual Enrollment – allows any card reader in the system to act like an enrollment reader
Event log – for V4 reporting

## Slide 17
O3 Access Dashboards Licensing Model
Based on number of doors
Access IO wont be counted towards eWEB licensing
Subscription 7.5% annually – just like eWEB
Grace period of 30 days if door limit exceeded – dashboard will be disabled
After 30 days grace period if door limit is within limit – dashboard continues to work
Notes: List price
eSYNC free
LPM model
eWEB license is required. Smallest would be fine